## Slide 1
Nate Phillips
Lindsey Hodges
Wani Hakim
ECE 410
January 29, 2011
Autonomous Emergency Response Robot
IEEE SoutheastCon Hardware Competition

## Slide 2: SoutheastCon Hardware Competition
Theme:
  Natural disasters can devastate whole countries.
  Fast emergency response is critical for preventing further crisis and saving lives.
Notes: Such as the recent mudslides in Brazil.

## Slide 3: Design Specifications
Purpose:
  Build an autonomous emergency response robot that can safely evaluate the situation and relay vital information to emergency response teams.
Goals:
  Navigate through specified floor plan
  Identify and avoid obstacles
  Sense hazards
  Find and determine status of victims
  Report vital information to emergency responders
Restrictions:
  Size: 20 x 20 x 20 cm
  Time Limit: 4 minutes
  Robot can not jump, fly, hover, or climb over walls.
  Wireless communication is not allowed.

## Slide 4: Scoring
Category | Points | Total Possible
Audio Output | 150 | 150
Digital Display | 50 | 50
Victim Position* | 60 | 720
Victim Status | 40 | 480
Hazard Location | 200 | 200
Total |  | 1,600
Notes: 15 points
will be deducted per grid square away from the correct position, with a minimum position
score of 0, using Manhattan Distance = |X2-X1| + |Y2-Y1|. Any “extra” reported victims receive a penalty of -30 points.

## Slide 5: Course Layout
1
4
3
2
RED: designated starting area
10 x 10 grid for victims and hazards
obstacles can be placed at any angle in hallways and rooms
START

## Slide 6: Navigation Platform
Platform has the same orientation even when body rotates.
B = North
A = West
C = East
D = South
Distance measurements used in calibration:
  DB = constant 2 cm
  DA + DB + DC = hallway width or distance between room walls

## Slide 7: Calibrating Sensors
Arduino code:
  float volts = analogRead(IRpin)*0.0048828125;
  float distance = 28*pow(volts, -1.0);
The IR sensors sit further inward to prevent the spike in error between 0 cm and 8 cm.
Voltage rating of 5V divided by 1024 points to give a value per step
  5V/1024 = 0.0048828125
Exponential
  Slope: 1/Volts * 28
  Distance = (Volts x)*28

## Slide 8: Obstacle Detection
Obstacle Detector
180° Servo Motor
Victim Detector
360° Servo Motor
Navigation Platform

## Slide 9: Obstacle Avoidance
Objects to Avoid:
  Walls
  3 cm x 2 cm victims
  4 cm x 9 cm obstacles
  2 cm x 4 cm obstacles

## Slide 10: Obstacle Avoidance
The robot must know where the obstacles and the walls are to navigate through the course.
The servo motor pans from 30° to 150° so the infrared sensor can take measurements.
Values returned are distance measurements
( ex. [121, 83, 2, 2, 2, 2, 54, 85, 141] )
where the value indicates how close the object is to the robot.
Program analyzes the values returned and the angle of the servo motor to decide whether the robot can fit around the obstacle or if it needs to try a different route.
The image shows how the infrared sensor input to the microcontroller when mounted on a servo motor matches the actual placement of the obstacles.

## Slide 11: Detecting Victims
Victims: Green LED in PVC cap
  ON = Conscious
  OFF = Dead
    No battery connections
  Blinking = Unconscious
    2 Hz with 50% duty cycle
    Blinks twice every second
Detection: Green LED used to detect the victim green LED
  a) Connect to two bidirectional I/O pins and drive LED with current in forward direction
  b) Drive LED in the reverse-bias direction
  c) Current discharges and is measured
Time to discharge is inversely proportional to amount of incident light measured

## Slide 12: Robot Output
Display
Speaker
Audio Controller
Voice synthesizer
Developed by RC Systems
Model: V8600A
4 digit LED display
1” Alphanumeric numbers
Controlled by stackable serial drivers
Bright segments
Covered with antiglare material to increase readability
8 ohm

## Slide 13: Robot Body
Wheels
Micro DC Geared Motors
Battery Pack
Gear ratio: 1:120
No-load speed (6V): 180RPM
Stall current(6V):470mA
Torque (6V): 1.92Kgcm
8 cm. diameter diamond-tread wheels
8 AA batteries
Nominal voltage = 12V

## Slide 14: Overall Program Design
move forward
center of course
detect obstacle
detect victim
detect hazard
detect obstacle
move forward
enter room
detect obstacle
program complete
report info
YES
NO
NO
NO
NO
move forward
YES
YES
YES
NO
report info
YES
detect obstacle
NO
move forward
YES
avoid obstacle
avoid obstacle
avoid obstacle
avoid obstacle

## Slide 15: Cost
Cost to reproduce
Minus course materials
  prototype cost = $361.30
Relatively low
  Salvaged components
  from previous projects
Part | Cost
Wiring | $10.00
SHARP Infrared Sensors (6) | $24.00
Electromagnetic Field Detector | $10.00
Green LEDs | $2.00
V8600A Audio Synthesizer | $100.00
LED Digital Display | $30.00
Batteries | $35.00
360 full rotation servo motor | $13.50
180 servo motor | $15.60
Robot Body and Motors | $49.20
Arduino Mega Microcontroller | $55.00
DFRobot 2A Motor Controller | $17.00
4 x 8 sheets of plywood | $120.00
1 gallon of purple matte paint | $30.00
TOTAL | $511.30